## Slide 1: Biomechanics
7ο εξάμηνο
Σχολή Μηχανολόγων Μηχανικών ΕΜΠ
Διδάσκων:
Michael Neidlin
Fritz Kahn (1888 – 1968)
FE Analysis Practical Course

## Slide 2: Practical course structure
CT data provided
Segmentation/
smoothing
STL model
of femur
Material models (in vitro tests
from literature)
Loading conditions (Forces
acting on the femur head)
P: 70180 kg
Standing and jumping
FEA analysis
in PC lab
Short report
with results
(in groups)
Homework IV
We are here now

## Slide 3: Exact information on basic computation scenario
Scenario is: Force acting on femur head for person between 70-180 kg (standing
and landing during jump)
Lower part of femur is fixed. Shell meshing with 4mm thickness is applied.
We want to compute the maximum von Mises stress at the femur neck depending
on weight for the two conditions.
Femur neck
weight
stress
Result: smth like this

## Slide 4: Loading information and material parameters
If you do not want to find your “own” data, here is the input:
Will be needed for material fitting,
you will learn how to do later on
Bone as hyperelastic isotropic material
Standing results in joint force
of 2.4*BodyWeight
Jumping results in joint force of
7*BodyWeight

## Slide 5: Tutorials – Have the files ready for the lab
https://www.dropbox.com/s/7b8qvx5ouz0v76m/FETutorials.zip?dl=0
Read these before the FE Lab if you are a total beginner
Basic tutorials to do in the first session,
you can read them at home and do them in the lab
From page 9-21 description how to fit material data
From p. 12-22 for the advanced Ansys User

## Slide 6: I am done with the tutorials, what now? (For basic users!)
Do the simulations with your model or use this
https://www.dropbox.com/s/8sty8uv13eobsgt/femur_shell_final_own.stl?dl=0
The simulation process is the following (Help is provided on the next slides):
1. Read in the stl model and load into Static Structural
2. Define surface thickness (if necessary of e.g. 4 mm)
3. Mesh the model. Automatic method, shell mesh should be produced
4. Create Named selections for fixed b.c., Femur neck and Joint loading location (simplest case is Nodal Force at one node). Create boundary conditions
5. Create hyperelastic material through material fitting
6. Run the simulation for one case. See if it works out. Result evaluation through User Defined Results
7. Do Mesh Independence then do your study!

## Slide 7: How to read in stl file
Use FE Modeler from WB
After startup of FE Modeler
1
2
3
Connect like this

## Slide 8: This is how setup looks like (cheat slide)
Here you can choose what you want to select (node, edge etc.)
for the named selection step!
Additional information for named selections:

## Slide 9: User Defined Results (How to just evaluate stresses at the femur neck)
This is the
von Mises stress
This is the location
This is the result

## Slide 10: What is mesh independence?
When your simulation works out you have to ensure that the results are mesh independent!
Rerun the simulation finer meshes (e.g. decrease and increase the max. element size by of 2)
and evaluate your results (e.g. max neck stress) for the different meshes.
When the results are not changing, this means that you have a mesh independent result!
Then you can continue with the study.
If the explanation as too short, do research online!

## Slide 11: Suggestions for advanced users
Boundary condition of Nodal Force is very simple. One way to improve it would be to separate a section of the stl that experiences the load from the acetabulum
Material anisotropy was not considered.
There are orthtropic/transeverse isotropic (however
ELASTIC not hyperelastic) models in Ansys.
However there is also a possibility to include an anisotropic hyperelastic
function through a user defined script in Ansys.
From page 12-22.
However no fitting is possible through Ansys so you would need your material parameters a priori. I WOULD RECOMMEND DOING THIS 
Modeling everything as a shell of continuous thickness is big simplification!
You could try to apply several thicknesses by splitting the model or
combine two materials (compacta and spongiosa) or other things....
If you have questions about other approaches, do not hesitate contacting me.

## Slide 12: What about the report?
After the FEA study please submit a short written report (about 2-5 pages) on methods, results and discussion.
You can do this in groups of 2-5 people if you wish.
There is no need in being exhaustive, however I am especially interested to see some critical thoughts on the short project that you did.
What can we generally get out of the results?
What were the limitations? What would you improve if you had a lot of time? How do you think these kind of analyses could help. And so on, be creative.
The deadline is 9.01.2018!